# AMI for CCM
DRAFT
## Asynch Interface and Operation Usage Mapping
CORBA already provides a suitable technique on the middleware layer called AMI (see xxxx.pdf). There are two different mechanisms for deferred synchronous calls. For each, the signature of operation is modified. In case of the "poller" mechanism, a caller obtains a poller object instead of a result. This object can be queried later to get the actual result.
The alternative mechanism is to retrieve results via callbacks. The request is sent using an asynchronous call, to a remote object, once the request is processed, the result is sent back to a callback (a so called reply handler). This example studies the second variant that uses a Callback; the sender receives callback calls in a so called reply handler.
To use AMI in CCM, an AMI component should be created. This component provides the asynchronous interfaces for the clients. The design of this component and the signature of the used interfaces and operations are all described in implied-IDL.
Each designed interface is mapped to implied-IDL interfaces and operations. An interface is prefixed by “AMI_”. If this implied-IDL interface name conflicts with existing interface in the same module, xxxx. Each operation in an interface is prefixed with “sendc_”. If this implied-IDL operation name conflicts with existing operations on the interface or any of the interface’s base interfaces, “ami_” strings are inserted between “sendc_” and the original operation name until the implied-IDL operation name is unique.

### Running Example
A running example is used throughout this section to clarify the generation of the new typed asynchronous invocation stubs, the new reply handling interfaces for receiving callback responses The example features a simple stock portfolio manager interface. Most importantly, the interface includes operations that cover all cases of operation signature:
- attributes
- in arguments
- inout arguments
- out arguments
- return values
- user exceptions
  Operations declared oneway are not mapped to asynchronous invocation stubs because they are already asynchronous in nature.
// Original IDL
exception InternalError { string sym; };
interface StockManager {
attribute string stock_exchange_name;

boolean	add_stock(in string symbol, in double quote);
void	edit_stock(in string symbol, in double new_quote)
raises(InvalidStock);
void	remove_stock(in string symbol, out double quote)
raises(InvalidStock);
boolean	find_closest_symbol(inout string symbol);
double	get_quote(in string symbol) raises(InvalidStock);
};
Implied-IDL for asynchronous interfaces
For each designed interface a new asynchronous interface in implied-IDL is created. The signature of this interface is as follows:
AMI_<ifaceName> where if ifaceName is the name of the interface.
The operations and attributes within this interface are described in the following sections.
Implied-IDL for callback interfaces
For each designed interface a new callback interface in implied-IDL is created. The signature of this interface is as follows:
AMI_<ifaceName>_callback where if ifaceName is the name of the interface.
The operations and attributes within this interface are described in the section xxx.
 Implied-IDL for operations
The signature of the implied-IDL for a given IDL operation is exactly the same as the AMI for CORBA:
- void return type, followed by;
- sendc_<opName> where opName is the name of the operation.
The asynchronous callback version takes the following arguments in order:
An object reference to a type-specific ReplyHandler as described in Section xxx, “Type-Specific ReplyHandler Mapping,” with the parameter name ami_handler. If a nil ReplyHandler reference is specified when this operation is invoked, no response will be returned for this invocation. A system exception may be raised by the ORB during evaluation of the request, but once sendc returns, no further results of the operation will be made available. This is equivalent to setting the CORBA::INV_NO_RESPONSE flag when making a DII deferred request.
- Each of the in and inout arguments in the order that they appeared in the operation's declaration in IDL, all with a parameter attribute of in and with the type specifier and parameter name of the original argument.
- out arguments are ignored (i.e., are not part of the async signature).
The implied-IDL operation signature has a context expression identical to the one from the original operation (if any is present).
Implied-IDL for attributes
In AMI for CCM, the same rules apply as in AMI for CORBA:
The signature of the implied-IDL for the callback model getter and setter operations corresponding to an interface’s attribute is as follows.
- Setter operations are only generated for attributes that are not defined readonly
- void return type, followed by the operation name, which to distinguish between the getter and setter operations for the attribute is given by either:
- sendc_get_<attributeName> for reading the attribute value, where attributeName is the name of the attribute, or
- sendc_set_<attributeName> for setting the attribute value, where attributeName is the name of the attribute that is not defined readonly. The callback implied-IDL operations take the following arguments in order:
- An object reference of a type-specific ReplyHandler as described in Section xxx “Type-Specific ReplyHandler Mapping,” with the parameter name ami_handler.
- The additional arguments for asynchronous implied-IDL operations for attributes are as follows:
- For the attribute’s generated get operation, there are no additional arguments.
- For the attribute’s generated set operation, there is one additional argument, in <attrType> attr_<attributeName>, where attrType is the type of the attribute, and attributeName is the name of that attribute. The set operation is only generated for attributes that are not defined readonly.

Exception Handling

Type specific ReplyHandler mapping

Example
// AMI implied-IDL including callback operations
// for original example IDL defined in Section xxx

exception InvalidStock { string sym; };

local interface AMI_StockManagerHandler;
interface StockManager {
// Original operation Declarations
attribute string stock_exchange_name;
boolean	add_stock(in string symbol, in double quote);
void	edit_stock(in string symbol, in double new_quote)
raises(InvalidStock);
void	remove_stock(in string symbol, out double quote)
raises(InvalidStock);
boolean	find_closest_symbol(inout string symbol);
double	get_quote(in string symbol) raises(InvalidStock);
};

// Async operation Declarations
local interface AMI_StockManager {
void	sendc_get_stock_exchange_name(
in AMI_StockManagerHandler ami_handler);
void	sendc_set_stock_exchange_name(
in AMI_StockManagerHandler ami_handler,
in string attr_stock_exchange_name);
void	sendc_add_stock(
in AMI_StockManagerHandler ami_handler, in string symbol,
in double quote);
void	sendc_edit_stock(
in AMI_StockManagerHandler ami_handler,
in string symbol, in double new_quote);
void	sendc_remove_stock(
in AMI_StockManagerHandler ami_handler,
in string symbol);
void	sendc_find_closest_symbol(
in AMI_StockManagerHandler ami_handler,
in string symbol);
void	sendc_get_quote(
in AMI_StockManagerHandler ami_handler,
in string symbol);
};

// Async callback operation Declarations
local interface AMI_StockManagerHandler {
void	get_stock_exchange_name(
in string ami_return_val);
void	get_stock_exchange_name_excep(
in CCM_AMI::ExceptionHolder excep_holder);
void	set_stock_exchange_name();
void	set_stock_exchange_name_excep(
in CCM_AMI::ExceptionHolder excep_holder);
void	add_stock(
in boolean ami_return_val);
void	add_stock_excep(
in CCM_AMI::ExceptionHolder excep_holder);
void	edit_stock();
void	edit_stock_excep(
in CCM_AMI::ExceptionHolder excep_holder);
void	remove_stock(
in double quote);
void	remove_stock_excep(
in CCM_AMI::ExceptionHolder excep_holder);
void	find_closest_symbol(
in boolean ami_return_val,
in string symbol);
void	find_closest_symbol_excep(
in CCM_AMI::ExceptionHolder excep_holder);
void	get_quote(
in double ami_return_val);
void	get_quote_excep(
in CCM_AMI::ExceptionHolder excep_holder);
};
Implied-IDL for a client component
The signature of the implied-IDL for a client component is as follows:
The usual component declaration : Component Client
- The client uses each declared asynchronous interface using the following declaration :
- uses AMI_<ifaceName> uses_asynch_<ifaceName>
where ifaceName is the name of the interface.
- The client should be able to use the synchronous interface. Therefore each interface should be declared as follows:
- uses <ifaceName> uses_synch_<ifaceName>
where ifaceName is the name of the interface.
Example
// Implied IDL for a client component
component Client {
uses AMI_StockManager uses_asynch_StockManager;
uses StockManager uses_synch_StockManager;
};
Implied-IDL for an AMI component
The signature of the implied-IDL for an AMI component is as follows:
- For each interface, the following declaration must be inserted in order to provide the asynchronous interface to a client :
- provides AMI_<ifaceName> prov_asynch_<ifaceName>
where ifaceName is the name of the interface.
- For each interface, the following declaration should be inserted to perform synchronous requests on the server component:
- uses <ifaceName> uses_synch_<ifaceName>
where ifaceName is the name of the interface.
Example
// Implied IDL for an AMI component
component AMI {
provides AMI_StockManager prov_asynch_StockManager;
uses StockManager uses_synch_StockManager;
};

Implied-IDL for a server component
The signature of the implied-IDL for a server component is as follows:
- For each interface, the server component just provides the interface. The server doesn't know whether the AMI component or the client component is used :
- provides <ifaceName> prov_synch_<ifaceName>
where ifaceName is the name of the interface.
Example
// Implied IDL for a Server component
component Server {
provides StockManager prov_synch_StockManager;
};

Implied-IDL3+

Once ready, IDL3+ (see xxx) should be used to describe the interface between the client and AMI component.
First, a “porttype” should be defined, named “AMI_<ifName>Port”, where ifaceName is the name of the interface. This porttype should have one “uses” declaration and one “provides” declaration.
The signature of these declarations are the same as described before.
Example
// Implied IDL for a porttype declaration
porttype AMI_StockManagerPort {
uses AMI_StockManager uses_asynch_StockManager;
provides AMI_StockManagerHandler prov_handler_StockManager;
};

The client component and AMI component should use this porttype, using the “port” and “mirrorport” key words. These ports should be declared as follows:
- The client component should have a port declaration. The name of this port is prefixed with “port_asynch_” followed by <ifaceName>, where ifaceName is the name of the interface.
- The AMI component should have a mirrorport declaration. The name of this mirrorport is prefixed with “mport_asynch_”, followed by <ifaceName>, where ifaceName is the name of the interface.
Example
// Implied IDL3+ for a client component
component Client {
port AMI_StockManagerPort port_asynch_StockManager;
uses StockManager uses_synch_StockManager;
};

// Implied IDL3+ for an AMI component
component AMI {
mirrorport AMI_StockManagerPort mport_asynch_StockManager;
uses StockManager uses_synch_StockManager;
};

## Connector Usage Example: AMI_Callback
The following example shows a connector of type "AMI callback", which performs an asynchronous method invocation with a callback on a MyFoo interface. It introduces the use of a connector. This example consists of a Sender and Receiver component with an AMI component in between. The Receiver component provides the interface MyFoo as follows:

interface MyFoo
{
long foo (in string in_str, out string answer) raises (InternalError);

attribute short rw_attrib;
readonly attribute short ro_attrib;
};
Example 1: MyFoo Interface Declaration
As mentioned, AMI in CCM is a connector. This component is placed between the Sender (client) and the Receiver (server) components (see figure below).

Sender
('client' component)
AMI
(AMI-component)
Receiver
('server' component)

v

MyFoo
AMI_MyFoo
AMI_MyFoo_callback

v

Synchronous

Figure 1 : AMICallback Example
As said before, the IDL interface needs to be extended for handling asynchronous invocations. A new (implied) interface (AMI_MyFoo) is created. For each existing method with in- and/or out-parameters or return values in MyFoo, a new void method with the prefix sendc_ is added to the implied AMI_MyFoo interface. The out-parameters are not used in these methods.
Attributes

The signature of the implied-IDL for the callback model getter and setter operations
corresponding to an interface’s attribute is as follows.
- Setter operations are only generated for attributes that are not defined readonly
- void return type, followed by the operation name, which to distinguish between the
- getter and setter operations for the attribute is given by either:
    - sendc_get_<attributeName> for reading the attribute value, where
attributeName is the name of the attribute, or
    - sendc_set_<attributeName> for setting the attribute value, where attributeName is the	name of the attribute that is not defined readonly.
The AMI component should provide and the Sender component should use this AMI_MyFoo interface.
Besides an AMI_MyFoo interface the (implied) callback interfaces should be created. The Sender component should provide and the AMI component should use this callback interface. The callback interface should be named, using AMI_ as prefix and Handler as postfix. In this example AMI_MyFooHandler. In this interface all prefixed sendc_ methods should be listed twice; once without a postfix and once with '_excep'. The callback_handler handles the callback calls. The signature of this method is to pass the return value of the foo method as a first parameter, followed by the out parameters of this method.
The callback_exception is called when the Receiver component caught an exception while executing foo.
The Receiver component (server) just provides the original interface (MyFoo); The AMI component uses this interface.
The needed interfaces are defined as follows:
// -- resulting (implied) interfaces
//

// Implied callback interface from AMI-component to calling component
interface AMI_MyFooHandler
{
void foo (in long ami_return_val, in string answer);
      void foo_excep (in CCM_AMI::ExceptionHolder exception_holder);

void get_rw_attrib (in short ami_return_val);
void get_rw_attrib_excep (in CCM_AMI::ExceptionHolder exception_holder);

void set_rw_attrib ();
void set_rw_attrib_excep (in CCM_AMI::ExceptionHolder exception_holder);

void get_ro_attrib (in short ami_return_val);
void get_ro_attrib_excep (in CCM_AMI::ExceptionHolder exception_holder);
};

// Implied AMI component interface. Calling component calls AMI-component and
// AMI-component calls the receiving component using the MyFoo interface.
interface AMI_MyFoo
{
void sendc_foo (in AMI_MyFoo_callback ami_handler, in string in_str);
void sendc_get_rw_attrib (in AMI_MyFooHandler ami_handler);
void sendc_set_rw_attrib (in AMI_MyFooHandler ami_handler, in short rw_attrib);
void sendc_get_ro_attrib (in AMI_MyFooHandler ami_handler);
};
Example 2: Implied interfaces
To use AMI, an AMI component is needed, implementing the previous (implied) methods (see Example 2).
Each time an asynchronous call is invoked, a reply handler should be passed. The reply handler should be created on the Sender side and should be passed to the AMI component component Sender (as the first parameter of the sendc function). The AMI component uses this reply handler to call the Sender when the answer is received. It's up to the user whether to create one “global” reply handler or one reply handler per request.
When nil is passed as reply handler, the AMI component treats that request as a oneway method. None of the provided callback methods are invoked.

// SENDER COMPONENT
module CCM_AMI
{
  component Sender
  {
    // for asynch invocation.
    uses CCM_AMI::AMI_MyFoo uses_asynch_MyFoo;

    // for synchronous invocation
    uses MyFoo uses_synch_MyFoo;
  };
};

// AMI COMPONENT
module CCM_AMI
{
  component AMI
  {
    //provides the interface for Sender
    provides CCM_AMI::AMI_MyFoo prov_asynch_MyFoo;

    //uses the interface of the Receiver ('server')
    uses MyFoo uses_synch_MyFoo;
  };
};

//RECEIVER COMPONENT
module CCM_AMI
{
  component Receiver
  {
    //provides
    provides MyFoo prov_synch_MyFoo;
  };
};
Example 3: Implied IDL, describing the components

IDL3+
Using IDL3+, the component description could look like this:
//BASE DEFINITIONS
porttype AMI_MyFooPort
{
uses CCM_AMI::AMI_MyFoo uses_asynch_MyFoo;
provides CCM_AMI::AMI_MyFooHandler prov_handler_MyFoo;
};

//SENDER COMPONENT
module Hello_AMI
{
component Sender
  {
port AMI_MyFooPort port_asynch_MyFoo;
uses CCM_AMI::MyFoo uses_synch_MyFoo;
  };
};

// AMI COMPONENT
module Hello_AMI
{
component AMI
{
mirrorport AMI_MyFooPort mport_asynch_MyFoo;
uses CCM_AMI::MyFoo run_my_foo;
};
};

//RECEIVER COMPONENT
The receiver component IDL doesn't need IDL3+.